## Slide 2
Presentation Outline
1
Introduction & Motivation
2
Background of Solar Photovoltaics
3
Literature Review
4
Research Gap
5
Research Objectives
6
Methodology (SCAPS-1D)
7
Device Structure & Configurations
8
Results — Parametric Optimization
9
Final Optimized Performance
10
Comparison with Literature
11
Conclusion & Future Scope
12
Q&A
LEADING UNIVERSITY
DEPARTMENT OF ELECTRICAL AND ELECTRONIC ENGINEERING
Page | 2

## Slide 3
Introduction & Motivation
Global Energy Context
Global electricity demand is rising rapidly due to population growth, industrialization, and urbanization.
Conventional power generation still relies heavily on fossil fuels — coal, natural gas, and petroleum.
Fossil-fuel burning accelerates greenhouse-gas emissions, global warming, and environmental pollution.
Depleting reserves raise serious concerns about long-term energy security.
Renewable sources (solar, wind) are clean, abundant, and increasingly cost-competitive.
Solar energy has emerged as one of the fastest-growing renewable alternatives
Bangladesh Energy Challenge
High dependence on imported fossil fuels for electricity generation.
Frequent load shedding, particularly during the peak summer months.
Power shortages cause significant inconvenience to industry and households.
Bangladesh imports a portion of its electricity from neighbouring countries.
Solar energy offers a decentralized, scalable, and environmentally friendly solution for the national grid.
Data source: Ember, Global Electricity Review 2025.
LEADING UNIVERSITY
DEPARTMENT OF ELECTRICAL AND ELECTRONIC ENGINEERING
Page | 3

## Slide 4
Background of Solar Photovoltaics
Solar cell technologies are classified into three generations based on absorber materials and fabrication technology.
1st Generation
Crystalline silicon (c-Si)
Highest commercial market share
High efficiency, long-term stability
High material cost, rigid substrates
Mature fabrication technology
Typical PCE: 15–24%
2nd Generation
Thin-film technologies
CdTe, CIGS, amorphous Si (a-Si)
Lower material usage
Lower manufacturing cost
Flexible substrate compatibility
Typical PCE: 10–22%
This work
3rd Generation
Perovskite, DSSC, organic, quantum-dot
High efficiency with low-cost fabrication
Tunable bandgap, solution-processable
Flexible
RbGeI3 absorber → this study
Environmentally friendly, lead-free
Typical PCE: 15–26%+
LEADING UNIVERSITY
DEPARTMENT OF ELECTRICAL AND ELECTRONIC ENGINEERING
Page | 4

## Slide 5
Literature Review
Work | Materials | Key Findings | Limitations
Shamas Mushtaq et al. (2023) | ETL: SnO₂Absorber: MASnBr₃HTL: NiO | PCE = 34.52%, FF = 88.30%, Voc = 1.1214 V | Very high theoretical efficiency. Absorber different from Ge-based system.
B.K. Ravidas et al. (2023) | ETL: TiO₂Absorber: CsSnI₃HTL: P3HT, PEDOT:PSS, Spiro-OMeTAD | Established link between DFT-calculated bandgap and device efficiency | Not focused on multi-HTL comparative analysis
Dibyajyoti Saikia et al. (2022) | ETL: TiO₂Absorber: CsGeI₃HTL: CuI | Voc = 0.667 V, Optimized PCE = 10.8%, FF = 73.49% | Did not build large HTL×ETL comparative matrix
M. Khalid Hossain et al. (2023) | ETL: TiO₂Absorber: CsPbI₃HTL: CBTS | Maximum PCE = 19.06%. Proper ETL/HTL selection reduced recombination. | Lead-based CsPbI₃. Limited ETL/HTL comparison.
Sarra Bouazizi et al. (2022) | ETL: PCBMAbsorber: CsSnI₃HTL: CuI | Optimized ETL/HTL doping ≈ 10¹⁹ cm⁻³. Best thickness ≈ 480 nm. Max PCE = 18.13%. | Very low defect density hard to realize. Efficiency drops at high temperature.
Hossain et al. (2023) | ETL: PCBMAbsorber: CsSnI₃HTL: CuI | Direct bandgap CsSnI₃ (~0.95 eV) confirmed by DFT. ITO/PCBM/CsSnI₃/CuI/Au achieved ≈ 10.1% PCE. | Defect density fixed (10¹⁵ cm⁻³) — not realistic.
Grishma Pindolia et al. (2022) | ETL: TiO₂Absorber: RbGeI₃HTL: NiO | Optimized thickness: RbGeI₃ = 500 nm, NiO = 100 nm, TiO₂ = 50 nm. PCE = 10.11%, FF = 63.68%. | Efficiency still lower than lead-based PSCs. Sensitive to defect density.
Advik Pathak et al. (2026) | ETL: TiO₂Absorber: MAGeI₃, FAGeI₃, CsGeI₃, RbGeI₃HTL: Spiro-OMeTAD | RbGeI₃ best performance with PCE ≈ 26.47%. Optimal thickness ≈ 400 nm. | Ge²⁺ oxidation to Ge⁴⁺ creates high defect density.
Nishad et al. (2025) | Various Cu-based HTLs using RbGeI₃ PSC | Investigated several Cu-based HTLs; proper HTL selection improves carrier extraction and efficiency. | Focused mainly on HTL selection; comprehensive optimization not performed.
Chen et al. (2025) | Gradient-doped RbGeI₃ perovskite solar cell | Proposed gradient doping in RbGeI₃ absorber to enhance charge transport and improve PV performance. | Doping profile optimization only; no multi-ETL–HTL evaluation.
Dash et al. (2025) | DFT + SCAPS study of RbGeCl₃, RbGeBr₃, RbGeI₃ | Combined DFT with SCAPS-1D; reported RbGeI₃ as most promising among RbGeX₃ family. | Material comparison only; not comprehensive device optimization.
LEADING UNIVERSITY
DEPARTMENT OF ELECTRICAL AND ELECTRONIC ENGINEERING
Page | 5

## Slide 6
Research Gap
Existing Limitations
Lead-based perovskites (MAPbI₃, FAPbI₃) achieve high PCE but suffer from toxicity and environmental hazards.
Tin-based alternatives (MASnI₃, CsSnI₃) degrade rapidly due to Sn²⁺ → Sn⁴⁺ oxidation.
RbGeI₃ is environmentally benign and thermally stable but remains under-explored.
Limited studies on systematic ETL/HTL screening and full parametric optimization for RbGeI₃ devices.
This Study Addresses
Comprehensive screening of 8 ETL×HTL configurations.
Systematic optimization of 11+ device parameters via SCAPS-1D.
Lead-free RbGeI₃ absorber with CuI HTL and TiO2 ETL an under-reported combination.
LEADING UNIVERSITY
DEPARTMENT OF ELECTRICAL AND ELECTRONIC ENGINEERING
Page | 6

## Slide 7
Research Objectives
Broad Objective
To explore an environmentally friendly RbGeI₃ absorber based lead-free perovskite solar cell using SCAPS-1D simulation.
Specific Objectives
1
Charge Transport Layer Selection
Screen efficient ETL and HTL combinations for RbGeI3.
2
Device Configuration Analysis
Compare 8 device structures and identify the optimum architecture.
3
Parametric Optimization
Optimize thickness, defect density, bandgap, and interface properties for maximum PCE.
LEADING UNIVERSITY
DEPARTMENT OF ELECTRICAL AND ELECTRONIC ENGINEERING
Page | 7

## Slide 8
Methodology — SCAPS-1D Simulation
Simulation Tool
SCAPS-1D (Solar Cell Capacitance Simulator, 1-D) — University of Gent, Belgium.
Models charge transport, recombination, and interface behaviour in multilayer thin-film solar cells.
Standard Test Conditions
Illumination: AM 1.5G spectrum, 1000 W/m².
Temperature: 300 K.
Performance metrics: VOC, JSC, FF, PCE.
Performance Equations
FF = (Vmp × Jmp) / (Voc × Jsc)
PCE = (Voc× Jsc × FF) / Pin × 100%
Fig — Overall research methodology.
LEADING UNIVERSITY
DEPARTMENT OF ELECTRICAL AND ELECTRONIC ENGINEERING
Page | 8

## Slide 9
SCAPS-1D Simulation Environment
SCAPS-1D Simulation Environment
LEADING UNIVERSITY
DEPARTMENT OF ELECTRICAL AND ELECTRONIC ENGINEERING
Page | 9

## Slide 10
Device Structure
Proposed Architecture
FTO / TiO₂ / RbGeI₃ / CuI / Au
FTO — Transparent front contact (fluorine-doped SnO2)
TiO2 — Electron Transport Layer (ETL)
RbGeI3 — Lead-free perovskite absorber
CuI — Hole Transport Layer (HTL)
Au — Back metal contact
Fig: Schematic cross-section of FTO/TiO₂/RbGeI₃/CuI/Au device
LEADING UNIVERSITY
DEPARTMENT OF ELECTRICAL AND ELECTRONIC ENGINEERING
Page | 10
Front Electrode: FTO
ETL: TiO2
Absorber: RbGeI3
HTL: CuI
Back Electrode: Au
Sunlight

## Slide 11
Device Configuration Screening
Device | Architecture | VOC (V) | JSC (mA/cm²) | FF (%) | PCE (%)
D1 | NiO / RbGeI₃ / PCBM / FTO | 0.81 | 30.10 | 83.68 | 20.52
D2 | NiO / RbGeI₃ / TiO₂ / FTO | 0.82 | 30.46 | 84.48 | 21.08
D3 | CuI / RbGeI₃ / PCBM / FTO | 0.81 | 30.10 | 83.96 | 20.55
D4 | CuI / RbGeI₃ / TiO₂ / FTO | 0.82 | 30.46 | 84.72 | 21.11
D5 | CBTS / RbGeI₃ / PCBM / FTO | 0.82 | 30.20 | 82.36 | 20.30
D6 | CBTS / RbGeI₃ / TiO₂ / FTO | 0.82 | 30.55 | 82.13 | 20.68
D7 | Spiro-OMeTAD / RbGeI₃ / PCBM / FTO | 0.81 | 30.07 | 85.01 | 20.77
D8 | Spiro-OMeTAD / RbGeI₃ / TiO₂ / FTO | 0.82 | 30.46 | 75.76 | 18.92
Selected: D4 — FTO/TiO2/RbGeI3/CuI/Au
Best initial PCE 21.11% — used as the baseline for full parametric optimization → final PCE 26.69%
The way of achieving 26.69% efficiency is shown from next slides
LEADING UNIVERSITY
DEPARTMENT OF ELECTRICAL AND ELECTRONIC ENGINEERING
Page | 11

## Slide 12
Results — Absorber Layer Thickness
Parameter Varied
RbGeI₃ thickness swept from 0.3 µm to 1.0 µm.
All other parameters held constant.
Key Observations
PCE rises sharply from 0.3 → 0.7 µm, reaching ≈ 20.7% at 0.7 µm.
Beyond 0.7 µm, PCE declines slightly due to increased bulk recombination.
Jsc increases monotonically (more photons absorbed).
Voc and FF decrease gradually with thickness.
OPTIMUM
0.7 µm
MAX PCE
20.7%
JSC TREND
Increasing
Fig — Variation of PCE, Voc, Jsc and FF with absorber layer thickness.
LEADING UNIVERSITY
DEPARTMENT OF ELECTRICAL AND ELECTRONIC ENGINEERING
Page | 12

## Slide 13
Results — Absorber Defect Density
Parameter Varied
Defect density Nt swept from 10¹² to 10¹⁸ cm⁻³.
All other parameters held constant.
Key Observations
PCE drops sharply from 20.51% → 7.58% as Nt increases.
VOC falls from 0.86 V → 0.55 V.
JSC and FF also decrease gradually at high defect densities.
Higher defect density → more trap states → more SRH recombination.
Best output occurs at 10¹² cm⁻³; however, 10¹⁴ cm⁻³ was selected for the final device to obtain a realistic output.
OPTIMUM Nt
10¹⁴ cm⁻³
MAX PCE
20.51%
VOC DROP
0.86 → 0.55 V
Fig— Variation of PCE, Voc, Jsc and FF with absorber defect density.
LEADING UNIVERSITY
DEPARTMENT OF ELECTRICAL AND ELECTRONIC ENGINEERING
Page | 13

## Slide 14
Results — Absorber Dielectric Constant
Parameter Varied
Dielectric constant εr swept from 15 to 23.1.
All other parameters held constant.
Key Observations
PCE gradually decreases from 19.92% (εr=15) → 19.79% (εr=23.1).
VOC decreases marginally from 0.818 V → 0.812 V.
FF shows very small improvement (79.87% → 79.98%).
JSC remains nearly unchanged ≈ 30.46 mA/cm².
Lower dielectric constant is slightly more favourable.
OPTIMUM εr
15
MAX PCE
19.92%
JSC TREND
≈ Constant
Fig — Variation of PCE, Voc, Jsc and FF with absorber dielectric constant.
LEADING UNIVERSITY
DEPARTMENT OF ELECTRICAL AND ELECTRONIC ENGINEERING
Page | 14

## Slide 15
Results — Absorber Electron Affinity
Parameter Varied
Electron affinity χ swept from 3.9 eV to 4.2 eV.
All other parameters held constant.
Key Observations
Highest PCE (19.79%) achieved at χ = 3.9 eV.
PCE gradually decreases to 17.81% at χ = 4.2 eV.
VOC drops significantly from 0.812 V → 0.710 V.
JSC remains ≈ 30.46 mA/cm² (negligible change).
FF increases (79.98% → 82.33%) but cannot offset VOC loss.
Higher χ shifts conduction band → unfavourable band alignment.
OPTIMUM χ
3.9 eV
MAX PCE
19.79%
VOC DROP
0.812 → 0.710 V
Fig — Variation of PCE, Voc, Jsc and FF with absorber electron affinity.
LEADING UNIVERSITY
DEPARTMENT OF ELECTRICAL AND ELECTRONIC ENGINEERING
Page | 15

## Slide 16
Results — Absorber/ETL Interfacial Defect Density
Parameter Varied
Absorber/ETL (RbGeI₃/TiO₂) interfacial defect
density swept from 10¹² to 10¹⁸ cm⁻².
All other parameters held constant.
Key Observations
PCE decreases sharply from 21.04% → 8.40%.
VOC drops from 0.827 V → 0.439 V.
JSC decreases from 30.46 → 28.09 mA/cm².
FF declines from 83.52% → 68.11%.
Interface defects act as recombination centres — strong sensitivity.
Best output at 10¹² cm⁻²; 10¹⁴ cm⁻² selected for realistic output.
OPTIMUM Nt
10¹⁴ cm⁻²
MAX PCE
21.04%
SENSITIVITY
High
Fig — Variation of PCE, Voc, Jsc and FF with Absorber/ETL interfacial defect density.
LEADING UNIVERSITY
DEPARTMENT OF ELECTRICAL AND ELECTRONIC ENGINEERING
Page | 16

## Slide 17
Results — HTL/Absorber Interfacial Defect Density
Parameter Varied
HTL/Absorber (CuI/RbGeI₃) interfacial defect density swept from 10¹² to 10¹⁸ cm⁻²
All other parameters held constant.
Key Observations
Performance stable up to Nt= 10¹⁵ cm⁻².
PCE decreases from 19.79% → 18.19% at 10¹⁸ cm⁻².
Voc drops from 0.812 V → 0.746 V.
Jsc slightly reduces from 30.46 → 30.33 mA/cm².
FF peaks at 81.11% (10¹⁷ cm⁻²) then drops slightly.
CuI forms a more tolerant interface than TiO₂.
Best output at 10¹² cm⁻²; 10¹⁴ cm⁻² selected for realistic output.
OPTIMUM Nt
10¹⁴ cm⁻²
MAX PCE
19.79%
SENSITIVITY
Moderate
Fig 3.6 — Variation of PCE, Voc, Jsc and FF with HTL/Absorber interfacial defect density.
LEADING UNIVERSITY
DEPARTMENT OF ELECTRICAL AND ELECTRONIC ENGINEERING
Page | 17

## Slide 18
Results — Absorber Bandgap
Parameter Varied
RbGeI3 bandgap swept from 1.3 eV to 1.8 eV.
All other parameters held constant.
Key Observations
Highest PCE (19.87%) achieved at bandgap = 1.4 eV.
VOC increases from 0.803 V → 0.997 V as bandgap widens.
FF rises from 79.89% → 86.24%.
JSC drops sharply (30.79 → 15.23 mA/cm²) — wider gap absorbs fewer photons.
PCE decreases beyond 1.4 eV due to dominant JSC loss.
1.4 eV provides optimum voltage–current balance.
OPTIMUM Eg
1.4 eV
MAX PCE
19.87%
JSC DROP
30.79 → 15.23
Fig 3.7 — Variation of PCE, Voc, Jsc and FF with absorber bandgap.
LEADING UNIVERSITY
DEPARTMENT OF ELECTRICAL AND ELECTRONIC ENGINEERING
Page | 18

## Slide 19
Results — ETL (TiO2) Thickness
Parameter Varied
TiO2 ETL thickness swept from 0.01 µm to 0.09 µm.
All other parameters held constant.
Key Observations
Highest PCE (21.12%) obtained at ETL thickness = 0.01 µm
PCE decreases to 18.72% at 0.04 µm, then partially recovers to 19.97% at 0.09 µm
VOC and FF show similar non-monotonic trend.
JSC remains nearly constant (30.46 → 30.44 mA/cm²)
Thicker ETL increases electron transport path → higher recombination losses.
OPTIMUM Thickness
0.01 µm (10 nm)
MAX PCE
21.12%
JSC TREND
≈ Constant
Fig 3.8 — Variation of PCE, Voc, Jsc and FF with ETL thickness.
LEADING UNIVERSITY
DEPARTMENT OF ELECTRICAL AND ELECTRONIC ENGINEERING
Page | 19

## Slide 20
Results — HTL (CuI) Thickness
Parameter Varied
CuI HTL thickness swept from 0.1 µm to 1.9 µm.
All other parameters held constant.
Key Observations
PCE increases marginally from 19.7899% → 19.7915% (negligible change).
JSC slightly increases from 30.4605 → 30.4629 mA/cm².
VOC and FF show only very small improvements.
CuI already provides effective hole transport at 0.1 µm.
Further thickness increase gives no significant benefit.
0.1 µm selected as optimum (less material, simpler device).
OPTIMUM Thickness
0.1 µm (100 nm)
MAX PCE
19.79%
SENSITIVITY
Very Low
Fig — Variation of PCE, Voc, Jsc and FF with HTL thickness.
LEADING UNIVERSITY
DEPARTMENT OF ELECTRICAL AND ELECTRONIC ENGINEERING
Page | 20

## Slide 21
Results — Conduction Band Effective DOS (NC)
Parameter Varied
Conduction band effective density of states NC swept from 1×10¹⁷ to 1×10²⁰ cm⁻³.
All other parameters held constant.
Key Observations
PCE decreases gradually from 20.65% → 18.15%.
VOC drops from 0.859 V → 0.764 V.
JSC remains nearly unchanged ≈ 30.46 mA/cm².
FF peaks at 79.97% (10¹⁹ cm⁻³) then drops to 78.04% (10²⁰ cm⁻³).
Higher NC shifts quasi-Fermi level → reduced VOC.
OPTIMUM NC
1×10¹⁷ cm⁻³
MAX PCE
20.65%
VOC DROP
0.859 → 0.764 V
Fig — Variation of PCE, Voc, Jsc and FF with conduction band effective density of states.
LEADING UNIVERSITY
DEPARTMENT OF ELECTRICAL AND ELECTRONIC ENGINEERING
Page | 21

## Slide 22
Results — Valence Band Effective DOS (NV)
Parameter Varied
Valence band effective density of states NV swept from 1×10¹⁷ to 1×10²⁰ cm⁻³.
All other parameters held constant.
Key Observations
PCE decreases noticeably from 23.54% → 18.86%.
VOC drops significantly from 0.944 V → 0.780 V.
FF decreases from 81.81% → 79.40%.
JSC remains nearly unchanged ≈ 30.46 mA/cm².
Higher NV reduces quasi-Fermi level splitting → lower Voc.
OPTIMUM NV
1×10¹⁷ cm⁻³
MAX PCE
23.54%
VOC DROP
0.944 → 0.780 V
Fig — Variation of PCE, Voc, Jsc and FF with valence band effective density of states.
LEADING UNIVERSITY
DEPARTMENT OF ELECTRICAL AND ELECTRONIC ENGINEERING
Page | 22

## Slide 23
Results — Quantum Efficiency (QE)
Parameter Varied
QE = ratio of collected charge carriers to incident photons at each wavelength
.
Indicates light absorption capability and carrier collection efficiency.
Key Observations
QE rises from 34.5% (300 nm) to ~100% (400 nm).
Broad plateau 99–100% between 400–650 nm (excellent visible absorption).
Gradual fall beyond 650 nm (98.53% → 76.17% at 850 nm).
Sharp cutoff near 900 nm — matches RbGeI₃ bandgap.
Lower UV QE due to surface recombination of high-energy photons.
PEAK QE
~100% (400–650 nm)
CUTOFF
~900 nm
UV QE
34.5–49%
Fig — Variation of quantum efficiency (QE) with incident wavelength of the optimized solar cell.
LEADING UNIVERSITY
DEPARTMENT OF ELECTRICAL AND ELECTRONIC ENGINEERING
Page | 23

## Slide 24
Results — Energy Band Diagram
Parameter Varied
Total device thickness: 1310 nm.
CuI (100 nm) + RbGeI₃ (700 nm) + TiO₂ (10 nm) + FTO (500 nm).
Key Observations
CuI/RbGeI₃ interface: ΔEc ≈ 1.8 eV (electron-blocking), ΔEv ≈ 0.01 eV (hole-friendly).
RbGeI₃/TiO₂ interface: ΔEc ≈ 0.10 eV (slight spike — beneficial), ΔEv ≈ 1.99 eV (hole-blocking).
Strong quasi-Fermi level splitting → high VOC.
Slight band bending at heterojunctions → built-in electric field drives carrier separation.
Favourable band alignment enables selective electron/hole collection.
Fig — Energy band diagram
LEADING UNIVERSITY
DEPARTMENT OF ELECTRICAL AND ELECTRONIC ENGINEERING
Page | 24

## Slide 25
Final Optimized Performance
After sequential optimization of all device parameters, the proposed FTO/TiO₂/RbGeI₃/CuI/Au solar cell achieved:
PCE
26.69%
Power Conversion Efficiency
VOC
1.1127
Volts
JSC
30.32
mA/cm²
FF
79.13%
Fill Factor
Optimized Device Parameters
Parameter | Optimized Value
Absorber thickness | 700 nm
Absorber bandgap | 1.4 eV
Absorber defect density | 10¹⁴ cm⁻³
Interfacial defect density (both interfaces) | 1 × 10¹⁴ cm⁻²
ETL (TiO₂) thickness | 10 nm
HTL (CuI) thickness | 100 nm
Electron affinity | 3.9 eV
Conduction band DOS, NC | 1 × 10¹⁷ cm⁻³
Valence band DOS, NV Absorber Dielectric Constant | 1 × 10¹⁷ cm⁻³ 15 eV
LEADING UNIVERSITY
DEPARTMENT OF ELECTRICAL AND ELECTRONIC ENGINEERING
Page | 25

## Slide 26
Comparison with Literature
Device Structure | VOC (V) | JSC (mA/cm²) | FF (%) | PCE (%) | Year/Ref. | Method
FTO/TiO2/RbGeI3/NiO/Ag | 0.5311 | 28.89 | 63.68 | 10.11 | 2022 [13] | Experiment
ITO/C60/RbGeI3/CBTS/Au | 0.99 | 33.20 | 82.8 | 24.62 | 2024 [72] | Simulation
FTO/TiO2/RbGeI3/PEDOT:PSS/Au | 0.813 | 30.84 | 74.19 | 18.44 | 2025 [73] | Simulation
FTO/TiO2/MASn3/CBTS/Au | 1.03 | 30.24 | 83.41 | 25.86 | 2026 [61] | Simulation
FTO/TiO2/MASnI3/CZTS/Au | 0.96 | 31.66 | 67.00 | 20.28 | 2025 [74] | Simulation
FTO/TiO2/CsSnI3/P3HT/Au | 0.972 | 34.70 | 78.21 | 26.40 | 2023 [15] | Simulation
FTO/TiO2/RbGeI3/CuI/Au (This work) | 1.1127 | 30.3156 | 79.13 | 26.69 | This work | Simulation
Key Takeaway
The proposed device achieves the highest reported PCE among comparable RbGeI₃ simulation studies, with the highest VOC (1.1127 V) — demonstrating the benefit of CuI as HTL.
LEADING UNIVERSITY
DEPARTMENT OF ELECTRICAL AND ELECTRONIC ENGINEERING
Page | 26

## Slide 27
Conclusion
Summary of Findings
A lead-free RbGeI₃ perovskite solar cell was numerically optimized using SCAPS-1D under AM 1.5G.
Among 8 ETL× HTL configurations, FTO/TiO₂/RbGeI₃/CuI/Au (D4) gave the best initial performance.
Sequential optimization of absorber thickness, defect density, bandgap, electron affinity, DOS, and interface defects yielded a final PCE of 26.69%.
TiO₂/CuI transport layers provide excellent band alignment — ΔEc ≈ 0.10 eV spike at absorber/ETL and ΔEv ≈ 0.01 eV at HTL/absorber.
The proposed device outperforms prior RbGeI₃ simulation studies (24.62%, 18.44%) and the experimental baseline (10.11%).
Lead-free RbGeI₃ is a viable absorber for next-generation environmentally friendly photovoltaics.
PCE
26.69%
Power Conversion Efficiency
VOC
1.1127
Volts
JSC
30.32
mA/cm²
FF
79.13%
Fill Factor
LEADING UNIVERSITY
DEPARTMENT OF ELECTRICAL AND ELECTRONIC ENGINEERING
Page | 27

## Slide 28
Future Scope
⚗
Experimental Validation
Fabricate the optimized FTO/TiO₂/RbGeI₃/CuI/Au device.
Characterize under real AM 1.5G conditions.
Identify practical limitations of material synthesis and interface quality.
⛨
Stability Analysis
Long-term thermal and moisture stability of RbGeI₃.
Mitigate Ge²⁺ → Ge⁴⁺ oxidation.
Encapsulation and storage stability studies.
⚙
Interface Defect Engineering
Passivation techniques for TiO₂/RbGeI₃ and RbGeI₃/CuI interfaces.
Reduce interfacial recombination further.
Explore self-assembled monolayers (SAMs).
✦
Advanced Transport Materials
Higher-mobility ETL alternatives (e.g., SnO₂, ZnO).
Organic HTLs.
Tandem-junction architectures with Si bottom cell.
LEADING UNIVERSITY
DEPARTMENT OF ELECTRICAL AND ELECTRONIC ENGINEERING
Page | 28

## Slide 29
References
LEADING UNIVERSITY
DEPARTMENT OF ELECTRICAL AND ELECTRONIC ENGINEERING
Page | 29
[1] “RENEWABLES 2024 GLOBAL STATUS REPORT.” Accessed: Jun. 13, 2026. [Online]. Available: https://www.ren21.net/gsr-2024/
[2] “World Energy Outlook 2024 – Analysis,” IEA. Accessed: Jun. 13, 2026. [Online]. Available: https://www.iea.org/reports/world-energy-outlook-2024
[3] M. A. Green et al., “Solar cell efficiency tables (Version 64)”, doi: 10.1002/pip.3831.
[4] R. A. Afre and D. Pugliese, “Perovskite Solar Cells: A Review of the Latest Advances in Materials, Fabrication Techniques, and Stability Enhancement Strategies,” Micromachines, vol. 15, no. 2, p. 192, Feb. 2024, doi: 10.3390/mi15020192.
[5] N.-G. Park, M. Grätzel, T. Miyasaka, K. Zhu, and K. Emery, “Towards stable and commercially available perovskite solar cells,” Nat Energy, vol. 1, no. 11, p. 16152, Oct. 2016, doi: 10.1038/nenergy.2016.152.
[6] S. Samaki, F. Tchangnwa Nya, G. M. Dzifack Kenfack, and A. Laref, “Materials and interfaces properties optimization for high-efficient and more stable RbGeI3 perovskite solar cells: optoelectrical modelling,” Sci Rep, vol. 13, no. 1, p. 15517, Sep. 2023, doi: 10.1038/s41598-023-42471-w.
[7] “Rethinking the A cation in halide perovskites,” Science, vol. 375, no. 6583, Feb. 2022, doi: 10.1126/science.abj1186.
[8] “Compositional engineering of perovskite materials for high-performance solar cells,” Nature, vol. 517, no. 7535, pp. 476–480, Jan. 2015, doi: 10.1038/NATURE14133.
[9] I. Ahmed, K. Prakash, and S. M. Mobin, “Lead-free perovskites for solar cell applications: recent progress, ongoing challenges, and strategic approaches,” Chem. Commun., vol. 61, no. 37, pp. 6691–6721, May 2025, doi: 10.1039/D4CC06835A.
[10] I. Ahmed, K. Prakash, and S. M. Mobin, “Lead-free perovskites for solar cell applications: recent progress, ongoing challenges, and strategic approaches,” Chem. Commun., vol. 61, no. 37, pp. 6691–6721, May 2025, doi: 10.1039/D4CC06835A.
[11] “The Promise of Lead-free Perovskites: Can They Replace Toxic Alternatives in Solar Cells and Lead the Future?,” SciSpace - Paper. Accessed: Jun. 13, 2026. [Online]. Available: https://scispace.com/papers/the-promise-of-lead-free-perovskites-can-they-replace-toxic-cr9xlq9fncpu
[12] S. Samaki, F. Tchangnwa Nya, G. M. Dzifack Kenfack, and A. Laref, “Materials and interfaces properties optimization for high-efficient and more stable RbGeI3 perovskite solar cells: optoelectrical modelling,” Sci Rep, vol. 13, no. 1, p. 15517, Sep. 2023, doi: 10.1038/s41598-023-42471-w.
[13] “Optimization of an inorganic lead free RbGeI3 based perovskite solar cell by SCAPS-1D simulation,” Solar Energy, vol. 236, pp. 802–821, Apr. 2022, doi: 10.1016/j.solener.2022.03.053.
[14] “RETRACTED: Performance optimization of lead-free MASnBr3 based perovskite solar cells by SCAPS-1D device simulation,” Solar Energy, vol. 249, pp. 401–413, Jan. 2023, doi: 10.1016/j.solener.2022.11.050.
[15] “Investigation of photovoltaic performance of lead-free CsSnI3-based perovskite solar cell with different hole transport layers: First Principle Calculations and SCAPS-1D Analysis,” Solar Energy, vol. 249, pp. 163–173, Jan. 2023, doi: 10.1016/j.solener.2022.11.025.
[16] “Performance evaluation of an all inorganic CsGeI3 based perovskite solar cell by numerical simulation,” Optical Materials, vol. 123, p. 111839, Jan. 2022, doi: 10.1016/j.optmat.2021.111839.
[17] M. K. Hossain et al., “Numerical simulation and optimization of a CsPbI3-based perovskite solar cell to enhance the power conversion efficiency,” New J. Chem., vol. 47, no. 10, pp. 4801–4817, Mar. 2023, doi: 10.1039/D2NJ06206B.

## Slide 30
References
LEADING UNIVERSITY
DEPARTMENT OF ELECTRICAL AND ELECTRONIC ENGINEERING
Page | 30
[18] S. Bouazizi, W. Tlili, A. Bouich, B. M. Soucase, and A. Omri, “Design and efficiency enhancement of FTO/PC60BM/CsSn0.5Ge0.5I3/Spiro-OMeTAD/Au perovskite solar cell utilizing SCAPS-1D Simulator,” Mater. Res. Express, vol. 9, no. 9, p. 096402, Sep. 2022, doi: 10.1088/2053-1591/ac8d52.
[19] “Deep Insights into the Coupled Optoelectronic and Photovoltaic Analysis of Lead-Free CsSnI3 Perovskite-Based Solar Cell Using DFT Calculations and SCAPS-1D Simulations,” ACS Omega, Jun. 2023, Accessed: Jun. 04, 2026. [Online]. Available: https://pubs.acs.org/doi/full/10.1021/acsomega.3c00306
[20] “Computational Analysis of Germanium-Based Perovskites (MAGeI₃, FAGeI₃, CsGeI₃, RbGeI₃) for High-Efficiency Solar Cells Using SCAPS-1D.” Accessed: Jun. 04, 2026. [Online]. Available: https://www.researchsquare.com
[21] “(1) Numerical Investigation of RbGeI3-Based Lead-Free Perovskite Solar Cell with Various Cu-Based Hole Transport Layers Using SCAPS-1D | Request PDF,” ResearchGate. Accessed: Jun. 14, 2026. [Online]. Available: https://www.researchgate.net/publication/388620396_Numerical_Investigation_of_RbGeI3-Based_Lead-Free_Perovskite_Solar_Cell_with_Various_Cu-Based_Hole_Transport_Layers_Using_SCAPS-1D
[22] S. Chen, W. Fan, W. Fang, M. Zhang, and J. Wu, “SCAPS-1D simulation of RbGeI3-based solar cells with gradient doping and no hole transport layer,” in International Conference on Power Electronics Technology and Grid Systems (PETGS 2025), SPIE, May 2025, p. 13. doi: 10.1117/12.3067927.
[23] P. K. Dash, P. Banarjee, A. Nyayban, and S. Panda, “Optoelectronic properties and performance optimization for photovoltaic applications of R3m-RbGeX$_3$ (X = Cl, Br, I) perovskites: A combined DFT and SCAPS-1D study,” arXiv.org. Accessed: Jun. 14, 2026. [Online]. Available: https://arxiv.org/abs/2505.09362v1
[24] “Modelling polycrystalline semiconductor solar cells,” Thin Solid Films, vol. 361–362, pp. 527–532, Feb. 2000, doi: 10.1016/S0040-6090(99)00825-1.
[25] “Modelling polycrystalline semiconductor solar cells,” Thin Solid Films, vol. 361–362, pp. 527–532, Feb. 2000, doi: 10.1016/S0040-6090(99)00825-1.
[26] M. K. Hossain et al., “Combined DFT, SCAPS-1D, and wxAMPS frameworks for design optimization of efficient Cs2BiAgI6-based perovskite solar cells with different charge transport layers,” arXiv.org. Accessed: Jun. 11, 2026. [Online]. Available: https://arxiv.org/abs/2212.13237v1
[27] W. Shockley and H. J. Queisser, “Detailed Balance Limit of Efficiency of p‐n Junction Solar Cells,” J. Appl. Phys., vol. 32, no. 3, pp. 510–519, Mar. 1961, doi: 10.1063/1.1736034.
[28] H. Zhang, H. Wang, M. Ma, Y. Wu, S. Dong, and Q. Xu, “Application of compact TiO$_2$ layer fabricated by pulsed laser deposition in organometal trihalide perovskite solar cells,” arXiv.org. Accessed: Jun. 12, 2026. [Online]. Available: https://arxiv.org/abs/1807.00287v1
[29] A. J. Olasoji and S. H. Im, “Perspective Chapter: TiO2 Electron Transporting Layers for Perovskite Solar Cells,” in Titanium Dioxide - Uses, Applications, and Advances, IntechOpen, 2024. doi: 10.5772/intechopen.1007266.
[30] “Effect of Single-Crystal TiO2/Perovskite Band Alignment on the Kinetics of Electron Extraction,” The Journal of Physical Chemistry Letters, Feb. 2024, Accessed: Jun. 12, 2026. [Online]. Available: https://pubs.acs.org/doi/full/10.1021/acs.jpclett.3c03536
[31] K. Valadi, S. Gharibi, R. Taheri-Ledari, S. Akin, A. Maleki, and A. E. Shalan, “Metal oxide electron transport materials for perovskite solar cells: a review,” Environ Chem Lett, vol. 19, no. 3, pp. 2185–2207, Jun. 2021, doi: 10.1007/s10311-020-01171-x.
[32] ACS, “SnO2–TiO2 Hybrid Electron Transport Layer for Efficient and Flexible Perovskite Solar Cells,” ACS Energy Letters, May 2022, Accessed: Jun. 12, 2026. [Online]. Available: https://pubs.acs.org/doi/abs/10.1021/acsenergylett.2c00637
[33] L. Ji, T. Zhang, and S. Li, “Band alignment of TiO2 by controling Cl content for high-efficiency perovskite solar cells,” J. Mater. Chem. C, vol. 12, no. 36, pp. 14597–14604, Sep. 2024, doi: 10.1039/D4TC01495B.
[34] S. Kinza Fatima, R. H. Alzard, R. Amna, M. H. Alzard, K. Zheng, and M. Abdellah, “Lead-free perovskites for next-generation applications: a comprehensive computational and data-driven review,” Materials Advances, vol. 6, no. 21, pp. 7634–7661, 2025, doi: 10.1039/D5MA00681C.

## Slide 31
References
LEADING UNIVERSITY
DEPARTMENT OF ELECTRICAL AND ELECTRONIC ENGINEERING
Page | 31
[35] S. Ali, K. Ahmad, R. A. Khan, and P. Kumar, “Simulation-Based Studies on FAGeI3-Based Lead (Pb2+)-Free Perovskite Solar Cells,” Crystals, vol. 15, no. 2, p. 135, Feb. 2025, doi: 10.3390/cryst15020135.
[36] “(1) Exploring RbGeI₃ based perovskite solar cells: a comprehensive DFT study and SCAPS analysis with copper-based hole transport layers | Request PDF,” ResearchGate. Accessed: Jun. 12, 2026. [Online]. Available: https://www.researchgate.net/publication/393796290_Exploring_RbGeI_based_perovskite_solar_cells_a_comprehensive_DFT_study_and_SCAPS_analysis_with_copper-based_hole_transport_layers
[37] “Unveiling the role of band offset in inorganic RbGeI3-based perovskite solar cells: a numerical study in SCAPS-1D.” Accessed: Jun. 12, 2026. [Online]. Available: http://ouci.dntb.gov.ua/en/works/lxNmAz27/
[38] “(1) Integration of SCAPS-1D and density functional theory for the performance evaluation of RbGeI3-based perovskite solar cell | Request PDF,” ResearchGate. Accessed: Jun. 12, 2026. [Online]. Available: https://www.researchgate.net/publication/383862270_Integration_of_SCAPS-1D_and_density_functional_theory_for_the_performance_evaluation_of_RbGeI3-based_perovskite_solar_cell
[39] N. A. Abdulkareem, “A DFT study of structural, electronic and optical properties of Lead-free and Ge based cubic perovskite RbGeX3 (X= I, Br and Cl),” Passer Journal of Basic and Applied Sciences, vol. 5, no. 1, pp. 46–51, Jun. 2023, doi: 10.24271/psr.2023.371069.1187.
[40] Q. Sun, A. Sadhu, S. Lie, and L. H. Wong, “Critical Review of Cu‐Based Hole Transport Materials for Perovskite Solar Cells: From Theoretical Insights to Experimental Validation”, doi: 10.1002/adma.202402412.
[41] A. Ghosh et al., “Solar power conversion: CuI hole transport layer and Ba3NCl3 absorber enable advanced solar cell technology boosting efficiency over 30%,” RSC Adv., vol. 14, no. 33, pp. 24066–24081, Jul. 2024, doi: 10.1039/D4RA03695F.
[42] M. Stolterfoht et al., “The perovskite/transport layer interfaces dominate non-radiative recombination in efficient perovskite solar cells,” arXiv.org. Accessed: Jun. 07, 2026. [Online]. Available: https://arxiv.org/abs/1810.01333v2
[43] J. Z. Mbese, “Advancements in Inorganic Hole-Transport Materials for Perovskite Solar Cells: A Comparative Review,” Energies, vol. 18, no. 9, p. 2374, Jan. 2025, doi: 10.3390/en18092374.
[44] R. Pau et al., “Solution-processed CuI as a hole transport layer for Sn–Pb perovskite solar cells,” Journal of Materials Chemistry A, vol. 13, no. 48, pp. 42118–42127, 2025, doi: 10.1039/D5TA06770G.
[45] “Recent Progress In The Development Of High- Efficiency Perovskite Solar Cell Using Copper Iodide (CuI) As Hole Transport Layer » JoSDC.” Accessed: Jun. 12, 2026. [Online]. Available: https://journals.stmjournals.com/josdc/article=2024/view=151196/
[46] W. Yang et al., “The CuI/NiO gradient hole transport layer for enhanced carrier efficiency in large-area perovskite solar cell,” Appl. Phys. Lett., vol. 128, no. 14, Apr. 2026, doi: 10.1063/5.0326539.
[47] R. Corporation, “Fluorine-Doped Tin Oxide Thin Films with High Surface Conductance and Low Transparency for Boosting Performance in Dye-Sensitized Solar Cell Applications,” ACS Applied Energy Materials, Jun. 2023, Accessed: Jun. 12, 2026. [Online]. Available: https://pubs.acs.org/doi/abs/10.1021/acsaem.3c00058
[48] ACS, “Influence of the Transparent Conductive Oxide Type on the Performance of Inverted Perovskite Solar Cells,” ACS Applied Energy Materials, Dec. 2023, Accessed: Jun. 12, 2026. [Online]. Available: https://pubs.acs.org/doi/abs/10.1021/acsaem.3c02292

## Slide 32
References
LEADING UNIVERSITY
DEPARTMENT OF ELECTRICAL AND ELECTRONIC ENGINEERING
Page | 32
[49] “(1) (PDF) Study of fluorine-doped tin oxide (FTO) thin films for photovoltaics applications,” ResearchGate. Accessed: Jun. 12, 2026. [Online]. Available: https://www.researchgate.net/publication/317348397_Study_of_fluorine-doped_tin_oxide_FTO_thin_films_for_photovoltaics_applications
[50] L. T. C. Tuyen, S.-R. Jian, N. T. Tien, and P. H. Le, “Nanomechanical and Material Properties of Fluorine-Doped Tin Oxide Thin Films Prepared by Ultrasonic Spray Pyrolysis: Effects of F-Doping,” Materials, vol. 12, no. 10, p. 1665, May 2019, doi: 10.3390/ma12101665.
[51] W. H et al., “Yttrium oxide engineered substrate enables improved durability for perovskite solar cells,” Nature communications, vol. 16, no. 1, Oct. 2025, doi: 10.1038/s41467-025-64548-y.
[52] T. Minemoto and M. Murata, “Impact of work function of back contact of perovskite solar cells without hole transport material analyzed by device simulation,” Current Applied Physics, vol. 14, no. 11, pp. 1428–1433, Nov. 2014, doi: 10.1016/j.cap.2014.08.002.
[53] E. Paz Totolhua et al., “Enhanced Efficiency of Mixed-Halide Perovskite Solar Cells Through Optimization of the Layer Thicknesses, Defect Density, and Metal Contact Work Function,” Materials, vol. 18, no. 7, p. 1601, Jan. 2025, doi: 10.3390/ma18071601.
[54] “(1) Investigation of the role of back contact work function for hole transporting layer free perovskite solar cells applications | Request PDF,” ResearchGate. Accessed: Jun. 12, 2026. [Online]. Available: https://www.researchgate.net/publication/358793021_Investigation_of_the_role_of_back_contact_work_function_for_hole_transporting_layer_free_perovskite_solar_cells_applications
[55] Waters, “Effect of Metal Electrodes on Aging-Induced Performance Recovery in Perovskite Solar Cells,” ACS Applied Materials & Interfaces, Dec. 2019, Accessed: Jun. 12, 2026. [Online]. Available: https://pubs.acs.org/doi/abs/10.1021/acsami.9b14619
[56] H.-J. Park, H. Son, and B.-S. Jeong, “SCAPS-1D Simulation for Device Optimization to Improve Efficiency in Lead-Free CsSnI3 Perovskite Solar Cells,” Inorganics, vol. 12, no. 4, p. 123, Apr. 2024, doi: 10.3390/inorganics12040123.
[57] P. Afrin, K. Farjana, A. Vumije, and M. N. Uddin, “An investigation on the impact of temperature variation over the performance of formamidinium tin iodide perovskite solar cell using SCAPS simulation,” AIP Advances, vol. 14, no. 7, Jul. 2024, doi: 10.1063/5.0209332.
[58] “The Physics of Solar Cells.” Accessed: Jun. 08, 2026. [Online]. Available: https://www.worldscientific.com/worldscibooks/10.1142/p276#t=aboutBook
[59] S. R. Hosseini et al., “Investigating the effect of non-ideal conditions on the performance of a planar CH3NH3PbI3-based perovskite solar cell through SCAPS-1D simulation,” Heliyon, vol. 8, no. 11, Nov. 2022, doi: 10.1016/j.heliyon.2022.e11471.
[60] “Comparative performance analysis of poly (3-hexylthiophene-2, 5-dial) and [6,6]-phenyl-C61 butyric acid methyl ester-based organic solar cells in bulk-heterojunction and bilayer structure using SCAPS,” Optik, vol. 302, p. 171691, May 2024, doi: 10.1016/j.ijleo.2024.171691.
[61] R. Islam, M. N. Uddin, M. J. Hossen, and A. Begum, “Photovoltaic performance of lead-free MASnI3-based perovskite solar cells with kesterite hole transport materials,” AIP Advances, vol. 16, no. 5, May 2026, doi: 10.1063/5.0315071.
[62] J.-Y. Huang, Y.-W. Yang, W.-H. Hsu, E.-W. Chang, M.-H. Chen, and Y.-R. Wu, “Influences of Dielectric Constant and Scan Rate to Hysteresis Effect in Perovskite Solar Cell: Simulation and Experimental Analyses,” arXiv.org. Accessed: Jun. 06, 2026. [Online]. Available: https://arxiv.org/abs/2106.12440v2
[63] K. Shivesh, I. Alam, A. K. Kushwaha, M. Kumar, and S. V. Singh, “Investigating the theoretical performance of Cs$_2$TiBr$_6$-based perovskite solar cell with La-doped BaSnO$_3$ and CuSbS$_2$ as the charge transport layers,” arXiv.org. Accessed: Jun. 07, 2026. [Online]. Available: https://arxiv.org/abs/2111.14381v1

## Slide 33
References
LEADING UNIVERSITY
DEPARTMENT OF ELECTRICAL AND ELECTRONIC ENGINEERING
Page | 33
[64] J. Shi, H. Zhang, X. Xu, D. Li, Y. Luo, and Q. Meng, “Interplays between charge and electric field in perovskite solar cells: charge transport, recombination and hysteresis,” arXiv.org. Accessed: Jun. 07, 2026. [Online]. Available: https://arxiv.org/abs/1604.02819v1
[65] “Physics of Semiconductor Devices,” Wiley Online Library. Accessed: Jun. 07, 2026. [Online]. Available: https://onlinelibrary.wiley.com/doi/book/10.1002/0470068329
[66] “Physics of Solar Cells,” Wiley Online Library. Accessed: Jun. 07, 2026. [Online]. Available: https://onlinelibrary.wiley.com/doi/book/10.1002/9783527618545
[67] M. A. Green, “Intrinsic concentration, effective densities of states, and effective mass in silicon,” J. Appl. Phys., vol. 67, no. 6, pp. 2944–2954, Mar. 1990, doi: 10.1063/1.345414.
[68] M. K. Hossain, M. H. K. Rubel, G. F. I. Toki, I. Alam, M. F. Rahman, and H. Bencherif, “Effect of various electron and hole transport layers on the performance of CsPbI3-based perovskite solar cells: A numerical investigation in DFT, SCAPS-1D, and wxAMPS frameworks,” arXiv.org. Accessed: Jun. 07, 2026. [Online]. Available: https://arxiv.org/abs/2211.02968v1
[69] A. Nakane et al., “Quantitative determination of optical and recombination losses in thin-film photovoltaic devices based on external quantum efficiency analysis,” arXiv.org. Accessed: Jun. 08, 2026. [Online]. Available: https://arxiv.org/abs/1604.04491v2
[70] O. J. Sandberg and A. Armin, “On the effect of surface recombination in thin film solar cells, light emitting diodes and photodetectors,” arXiv.org. Accessed: Jun. 08, 2026. [Online]. Available: https://arxiv.org/abs/1905.07291v1
[71] Z. Iqbal et al., “Interface Modification for Energy Levels Alignment and Charge Extraction in CsPbI$_3$ Perovskite Solar Cells,” arXiv.org. Accessed: Jun. 09, 2026. [Online]. Available: https://arxiv.org/abs/2307.13174v1
[72] L. Loumachi et al., “Strengthen the Power Conversion Efficiency of Solar Cell Based RbGeI3: Numerical Approach,” East Eur. J. Phys., no. 3, pp. 416–424, Sep. 2024, doi: 10.26565/2312-4334-2024-3-50.
[73] M. Raj, A. Aggarwal, A. Kushwaha, and N. Goel, “Moisture-resistant sustainable solar cell with RbGeI3 absorber layer,” J Mater Sci, vol. 60, no. 22, pp. 9176–9196, Jun. 2025, doi: 10.1007/s10853-025-11002-5.
[74] A. C. Piñón Reyes et al., “Study of a Lead-Free Perovskite Solar Cell Using CZTS as HTL to Achieve a 20% PCE by SCAPS-1D Simulation,” Micromachines, vol. 12, no. 12, p. 1508, Dec. 2021, doi: 10.3390/mi12121508.

## Slide 34
Thank You
Questions and Answers
LEADING UNIVERSITY
DEPARTMENT OF ELECTRICAL AND ELECTRONIC ENGINEERING
Page | 34